## Slide 1: Corner Beam Bracket Assembly
Featuring:
The H2-GCB Bracket
USPTO No. 10,024,046: Bracket Bracing System - Copyright© 2018 HDG, Inc. All Rights Reserved - Terms of Use Listed @ www.hdgep.com
209 Tidwell Drive Alpharetta, Georgia 30004 Office 770-777-7007 ~ ext. 234 E-mail: info@hdgep.com

## Slide 2
INSTALLATION GUIDE FOR SINGLE STORY BRACKETS
Read Guide Completely Before Installation
Instructions are not intended to replace deck construction plans.
Shown for product illustration purposes only.
Contact: info@hdgep.com or 770) 777-7007 Ext 234 for Additional Information
See www.hdgep.com for Instructional Video and Individual Product Specifications
Check for Additional Requirements
  Per Deck Design Professional AND local code authority
Water Intrusion
  **INSTALLER IS RESPONSIBLE FOR PREVENTING WATER INTRUSION**
    Verify all bolts and caulks are tightened
Fasteners:
  Installed ONLY in provided and specified holes
  Are to meet or exceed local code requirements.
  Recommended: HDG ASTM 123 Hot Dipped Galvanized or Stainless Steel
Certifications:
  HDG, Inc. Engineered Products: Subject to 1 Year Limited Warranty
  USPTO: No. 10,024,046: Bracket Bracing System
  Copyright © 2018 HDG, Inc. ~ All Rights Reserved
  Terms of Use: Listed @ www.hdgep.com

## Slide 3
Lay framing upon constructed beam and ledger. A cantilevered deck is used to display the function of this bracket. It can be used for similar purposes.
In this case, we are using (2) 2x12’s for beam and rim joist.
Double Rim Joist
Beam
(Side of Deck)
(Front of Deck)
Nail overlapped boards typically to hold them in place.

## Slide 4
Double Rim Joist
Beam
(Side of Deck)
(Front of Deck)
For Single Rim Joist use a 12” long block to permit proper frame spacing.
Place the H2-GCB bracket flush against corner, ensuring the bracket
is flush along the bottom of the rim joist and beam.
(Optional: can use screws or nails to temporarily hold in place.)

## Slide 5
Double Rim Joist
Beam
(Side of Deck)
(Front of Deck)
Cut 4x4 handrail posts and toenail or clamp them so that they align with the bolt holes on the bracket side flanges.
~3”
~

## Slide 6
Drill, using each bolt hole in bracket as guides, through all lumber with a minimum ½” hole for ½” bolts or 5/8” hole for 5/8” bolts.

## Slide 7
Installing bolts through the outside, fasten them inside the deck with code approved fasteners.

## Slide 8
(4) 7.5” HDG Bolts
A307 bolts 5/8” thick should be torqued to 73 ft/lbs. A307 bolts ½” thick should be torqued to 37 ft/lbs.
Torque per recommended wood council specs. Bolts are ½” diameter minimum.

## Slide 9
Installation Complete!

## Slide 10
Corner Beam Bracket Assembly Guide
* Read Guide Completely Before Installation *
Certifications
Instructions are not intended to replace deck construction plans.
Shown for product illustration purposes only.
Contact: info@hdgep.com or 770) 777-7007 Ext 234 for Additional Information
See www.hdgep.com for Instructional Video and Individual Product Specifications
  HDG, Inc. Engineered Products: Subject to 1 Year Limited Warranty
  USPTO: No. 10,024,046: Bracket Bracing System
  Copyright © 2018 HDG, Inc. ~ All Rights Reserved
  Terms of Use: Listed @ www.hdgep.com