## Slide 1: Deck Lateral Load Bracket Assembly
USPTO No. 10,024,046: Bracket Bracing System - Copyright© 2018 HDG, Inc. All Rights Reserved - Terms of Use Listed @ www.hdgep.com -
209 Tidwell Drive Alpharetta, Georgia 30004 Office 770-777-7007 ~ ext. 234 E-mail: info@hdgep.com
Featuring:
The H7-LLB Bracket

## Slide 2
Located within 2’ of end of deck

## Slide 3
Identify the H2 series bracket or ledger bolt closest to the floor joist you want to attach to.

## Slide 4
Position the lateral load bracket utilizing the available space within 2’ of the end of the deck per 2018 IRC.
Use the ledger bolt to fasten to the inside of the rim joist.
Example of a Deck Lateral Load Bracket
H7-LLB Installed Facing Down

## Slide 5
Drill 2 additional holes for bolts in floor joist after reinforcing with ½” (min) plywood on each side or use 8 structural screws each.

## Slide 6
Fasten 2 bolts per bracket minimum. Use ½” thread HDG steel bolts or use 8 structural screws each.

## Slide 7
Bottom view illustration.
Rim Joist
Top plate
Floor Joist
First Floor Wall Stud
H7-LLB Lateral Load Bracket
Ledger
Top Bolt

## Slide 8
Top view with plywood subfloor removed to illustrate side bolts.
Zoom View

## Slide 9
Top view to illustrate use with other post brackets.
Queen Bracket
Lateral Load Bracket
Wall Studs
Floor Joists
4” Space For Brick
Ledger
1/2” HDG Steel Bolts or 8 Structure Screws each
Corner Bracket
With Gusset Plate
(H2-GCR)
(H1-GQ)
(H7-LLB)

## Slide 10
With 4” Space Filled in Top View
Queen Bracket
Lateral Load Bracket
Wall Studs
Floor Joists
4” Space For Brick
Ledger
1/2” HDG Steel Bolts or 8 Structural Screws each
Corner Bracket
With Gusset Plate
(H2-GCR)
(H1-GQ)
(H7-LLB)

## Slide 11
Deck Corner Restraint Assembly – Front Side View
As applied to Siding
H7-LLB
Lateral Load Bracket
Rim Board
Floor Joists
Siding (Non-brick house)
Ledger
1/2” HDG Steel Bolts
H2-GCL
Corner Bracket
With Gusset Plate
4x4
Handrail Post
Rim Joist

## Slide 12
Deck Corner Restraint Assembly – Side View
As applied to Brick (With Queen Bracket)

## Slide 13
Deck Corner Restraint Assembly – Top View
As applied to Brick (With Queen Bracket)

## Slide 14
Deck Corner Restraint Assembly – Full Deck Top View
As applied to Brick (With Queen Bracket)

## Slide 15
INSTALLATION GUIDE FOR DECK LATERAL LOAD BRACKETS
Read Guide Completely Before Installation
Instructions are not intended to replace deck construction plans.
Shown for product illustration purposes only.
Contact: info@hdgep.com or 770) 777-7007 Ext 234 for Additional Information
See www.hdgep.com for Instructional Video and Individual Product Specifications
Check for Additional Requirements
  Per Deck Design Professional AND local code authority
Fasteners:
  Installed ONLY in provided and specified holes
  Are to meet or exceed local code requirements.
  Recommended: Fasten Master Headlock 2-7/8” Structural Wood Screws
Certifications:
  HDG, Inc. Engineered Products: Subject to 1 Year Limited Warranty
  USPTO: No. 10,024,046: Bracket Bracing System
  Copyright © 2018 HDG, Inc. ~ All Rights Reserved
  Terms of Use: Listed @ www.hdgep.com

## Slide 16
Lateral Load Bracket Assembly Guide
* Read Guide Completely Before Installation *
Certifications
Instructions are not intended to replace deck construction plans.
Shown for product illustration purposes only.
Contact: info@hdgep.com or 770) 777-7007 Ext 234 for Additional Information
See www.hdgep.com for Instructional Video and Individual Product Specifications
  HDG, Inc. Engineered Products: Subject to 1 Year Limited Warranty
  USPTO: No. 10,024,046: Bracket Bracing System
  Copyright © 2018 HDG, Inc. ~ All Rights Reserved
  Terms of Use: Listed @ www.hdgep.com